## Slide 1
Rebecca Zhang
June, 2010
Notes: <number>

## Slide 2: RTK Operation Radio Mode
1. Features of CHC RTK Receivers
3. Setup Base
4. Setup Rover
2. Software in RTK
5. Common Problems and Solutions

## Slide 3: X90 GNSS Receiver
Key Features
Build in Bluetooth®, cable free.
Unique Auto Base function
GPRS Module Inside
1W UHF internal transmitter for Base (Optional)
Features of CHC RTK Receivers
Notes: <number>

## Slide 4: X91 GNSS Receiver
Key Features
Unique Auto Base function
Compatible with PDL Datalink
GPRS Module Inside
Band Width: 410-430MHz/430-450MHz/450-470MHz
Smaller and lighter
Features of CHC RTK Receivers

## Slide 5: X90 GPS Receiver
Key Features
CHC Self Developed Engine Inside
24 Channels
Upgradable to PPK, RTK
Super Static Observation Ability
Minimum tracking threshold
Features of CHC RTK Receivers
Notes: Long Baseline – (Up to 200 km)
Short Observation Time - 5 minutes observation time *
* Within 30 km
<number>

## Slide 6: RTK Operation Radio Mode
2. Software in RTK
3. Setup Base
4. Setup Rover
1. Features of CHC RTK Receivers
5. Common Problems and Solutions

## Slide 7: Software in RTK
HcGPSset Software
Field Software for Receiver setup

## Slide 8: Software in RTK
HcGPRS Software
Field software for Radio and GPRS setup

## Slide 9: Software in RTK
LandStar Software
Field software RTK data collection

## Slide 10: Software in RTK RTK Steps
First time setup
Set Radio Setting
Set Receiver Setting
Set Survey work
Landstar
HCGPRS
HcGPSset

## Slide 11: Software in RTK RTK Steps
Not First time setup
Set Radio Setting
Set Receiver Setting
Set Survey work
Landstar
HCGPRS
HcGPSset

## Slide 12: Software in RTK RTK Steps
Not first time setup
Set Survey work
Landstar

## Slide 13: RTK Operation Radio Mode
3. Setup Base
2. Software in RTK
4. Setup Rover
1. Features of CHC RTK Receivers
5. Common Problems and Solutions

## Slide 14: Setup Base
Cable connection for Base and Radio station

## Slide 15: Setup Base

## Slide 16: Setup Base Base Station
Set Base Station by Software
Two working mode
Start the Base Station at Known Point
Start the Base Station at Unknown Point
Manually
Auto Base
HcGPSset/Hcloader
Landstar

## Slide 17: Setup Base Base Station
At known Point
Site Calibration
7/3 Parameter
Turn off and turn on the Base again
Start the Base at Known Point

## Slide 18: Setup Base Base Station
At unknown Point
Site Calibration
7/3 Parameter
Turn off and turn on the Base again
Reset Grid
Auto Base
Hcloader Software in the office
HcGPSset Software in the field

## Slide 19: Setup Base Base Station
Attention Points
If start the base manually, it is suggested to use cables to connect the base and the controller.
The car battery has enough battery for the field work.

## Slide 20: Setup Base Radio Station
Attention Points
The sequence of the cable connection
Connect the power cable to the Car battery in right pairs
The car battery has enough battery for the field work
Set the Radio Power Settings according to the working distance

## Slide 21: Setup Base Radio Station
Check whether the Radio Station is sending signal or not
Red light is flashing one second once
The power voltage on the screen changes
The green light on the Rover flashing one second once

## Slide 22: RTK Operation Radio Mode
4. Setup Rover
2. Software in RTK
3. Setup Base
1. Features of CHC RTK Receivers
5. Common Problems and Solutions

## Slide 23: Setup Base Rover Station
Set Rover Station by Software
HcGPSset/Hcloader
Landstar
HCGPRS
Set the RTK work
Set the Radio
Set the receiver

## Slide 24: Setup Base Rover Station
LandStar software
Start Rover Station
Build New Job
New Job
Coordinate System Parameter
Save Job
Configure Rover Parameter
Rover Option
(1)

## Slide 25: Setup Base Rover Station
LandStar software
Survey work
New Job
Site Calibration
(2)
Transformation Parameter from WGS84 to Local Coordinate system
GPS Point
Export
Grid Point
Key In
Import
7 or 3 Parameters

## Slide 26: Setup Base Rover Station
LandStar software
Base at known point
Open Job
Start the Base at known point
Reset Grid
Turn off and Turn on the Base again
Base at unknown point

## Slide 27: RTK Operation Radio Mode
5. Common Problems and Solutions
2. Software in RTK
3. Setup Base
1. Features of CHC RTK Receivers
4. Setup Rover

## Slide 28: Common Problems and Solutions
The data format of the Base and the Rover are different
Frequency and baud rate are different for the Radio station and Rover
Power is not enough for the Radio Station or the Rover.
No Radio Signal in the Rover (1_Data format and Power)
Make sure the broadcast data format are the same, e.g. CMR.
Make sure the frequency and baud rate are the same
Make sure all the battery have enough power.
Problem
Solutions

## Slide 29: Common Problems and Solutions
The connections of cables and connectors are not connected for the base and radio station.
The radio transmitting antenna fell down.
Working distance and power consumption are not match.
No Radio Signal in the Rover (2_Base And Radio Station)
Check the connections and make sure that every part is correctly connected
Check and setup the radio transmitting antenna
Make sure long working distance is with high power value in the radio station, while short distance with low power value.
Problem
Solutions

## Slide 30: Common Problems and Solutions
The rover is in the radio blind area or interference area.
No Radio Signal in the Rover (3_Rover )
If the Rover can receiver the radio signal in other place, it mean this area is radio signal blind area or interference area, change to another surveying method
Problem
Solutions

## Slide 31
Questions?

## Slide 32: Thanks
http://www.chcnav.com